## Slide 1
Dual use of future natural gas pipeline rights-of-way for the transport of electricity via HTSC cables
Paul M. Grant
W2AGZ Technologies
EPRI Science Fellow (retired)
IBM Research Manager Emeritus
San Jose, California USA
Author Contact
Financial support provided by the IBM Pension Fund
Poster 2P-LS2-10 PDF

## Slide 2
Preavviso!
Make sure the QR Code app in your Android iToy contains a browser with pdf reader plugin!

## Slide 3
Abstract
It appears likely that “clean” fossil fuels, exemplified by natural gas, given their current global abundance and accessibility, will continue to be exploited for at least the next two decades. We discuss a scenario whereby future natural gas/petroleum pipeline deployment provides an opportunity for creating a common right-of-way to transport both chemical and electrical energy, the latter via high capacity HTSC dc cables. Given the emergence of highly-Carnot efficient combined-cycle-gas-turbine (CCGT) generation technology, a significant portion of the natural gas delivered, perhaps as much as 40% or more, will be combusted at the end point to produce electricity. It would be useful to contemplate generating this electricity “in bulk” at the gas field “well head,” taking into account the savings wrought by transmitting a lower volume fraction of gas with reduced frictional and pumping losses, and also economies of scale by concentrating CO2 capture and reprocessing at a single site, rather than at a multitude of gas delivery points. In this poster, we examine possible candidate scenarios in North America and Europe and the advantages such dual use rights-of-way might provide for increased, yet with minimal environmental impact, delivery of chemical and electrical energy. For an initial study of this concept, see:
P.M. Grant, “Cryo-Delivery Systems for the Co-Transmission of Chemical and Electrical Power,” AIP Conf. Proc. 823, 291 (2006); doi: 10.1063/1.2202428

## Slide 4: Preamble
Discovery
  Cu-Perovskites: 20-135 K (1986-1993)
  MgB2: 40 K (2001-2002)
  Fe-Pnictides: 4-55 K (2006-Present)
Power Application R&D
  Basic wire development; OPIT, IBAD, RABiTS: USA, Japan, Germany, Italy, S. Korea, Russia (1987-2008)
  ac & dc Cables; Many: USA, Japan, Europe, S. Korea, China, Russia (1992-Present)
Read This Column First!

## Slide 5
  Power Control & Energy Storage (FCLs, SMES); Many: USA, Japan, Europe, S. Korea, China, Russia (1992-Present)
  Utility Demonstrations of Above Technologies
    Investor-owned (Only in USA: EPRI membership)
    “Public” (USA: LIPA, National Grid; Japan: TEPCO, Chubu)
Government-sponsored R&D
  DOE (USA, 1987-2008)
  MITI, METI, ISTEC (Japan, 1987-Present(?))
  KEPRI (S. Korea, 1990-Present(?))
Commercial Development (1987-Present)
  USA (AMSC, STI,...)
  Japan (Furakawa, Fukushima, Sumitomo...
  Europe (Columbus,...)

## Slide 6
HTSC Commercial Applications in Power
  At the time of its discovery, HTSC was heralded to soon embody a multibillion dollar market in Power Applications.
  Yet today, despite billions of dollars of investment in R&D and demonstrations by governments worldwide, not one “investor owned utility” and only perhaps two or three “public utilities,” have permanently deployed HTSC apps on the Grid.
  Why not? (see “Upbraiding the Utilities”)
  Some reasons (private communications from several large US IOU’s):
Economic returns do not justify the investment, even if the cost of the wire were zero!
Installation is a hassle, and current technology works pretty well and is improving (viz., “Smart Grid”)
Any new technology “skill set” would require lengthy negotiations with labor unions at the “lineman” level.
So what’s/where’s the “compelling need” to deploy HTSC on the Grid?
Upbraiding the Utilities
2011 P. M. Grant’s Editorial in Cold Facts
Cold Facts

## Slide 7: Global Energy Needs: - Challenges & Approaches/Solutions -
Challenges
  An expanding global population aspiring to the energy-consumption standard of living existing in Europe and North America and targeted by the emerging societies of middle and western Asia, the Indian subcontinent, Africa and South America.
  Possible adverse climate impact arising from the combustion products of increased amounts of fossil fuels consumed in pursuit of their objective.
  Limited ability to address such needs via renewable alternatives and associated physical constraints and socio-eco-invasive impact imposed by widespread deployment of solar, wind, and bio-sourced alternative sources.
Approaches/Solutions
  Vast reserves of natural gas have been uncovered worldwide, and attendant cost-effective retrieval technologies have been developed.
  Let’s start using them!

## Slide 8: A New Worldwide Opportunity for HTSC?
Natural Gas & Electricity!
Chart: 
| Coal | Natural Gas | Nuclear | Hydroelectric | Renewables | Other
2012 | 0.38407 | 0.31155 | 0.19475 | 0.070003 | 0.055384 | 0.010612
2012 USA Electricity Generation by Primary Fuel Source
Wow!
USA

## Slide 9
2011 EU Electricity Generation by Primary Fuel Source
About 3/4 that of US
BTW, it’s around 23% Worldwide
Chart: 
| Nuclear | Solid Fuels | Gases | Renewables | Petroleum and Products | Other
 | 27.6 | 25.9 | 22.2 | 21.3 | 2.2 | 0.7
Questions:
“Gases” = NG?
Where is Hydro?
“Solid” = Coal?
Preavviso!
Note different “pie slice” color code from USA
Europe

## Slide 10
US Electricity Generation/End Use – 2011
Units = 1015 BTU
= 2.933 x 103 Twh
US Natural Gas Generation/End Use – 2011
Units = 1012 ft3
= 1.35 x 104 Twh
~25% 2011!
What/where are the equivalent data for the EU? (Couldn’t find any...???)

## Slide 11
Chart: Year
| 2009 | 2010 | 2011 | 2012
Coal | 0.4445 | 0.46763 | 0.43881 | 0.38407
Natural Gas | 0.23314 | 0.25003 | 0.25661 | 0.31155
Nuclear | 0.20222 | 0.20428 | 0.20003 | 0.19475
Hydroelectric | 0.069221 | 0.065869 | 0.080843 | 0.070003
Renewables | 0.036523 | 0.042319 | 0.049105 | 0.055384
Other | 0.014396 | 0.014107 | 0.012656 | 0.010612
2013
Might be 37.5% by year end 2013 (check with USA-EIA)
Growth rate looks like
7%/yr!
USA

## Slide 12
Growth rate of electricity generation by Natural Gas looks “flat” at present. Will discovery of additional reserves and deployment of fracking, especially in Poland and the Ukraine, lead to a future “upward slope?”
Europe

## Slide 13: Advantages of HTSC vis-a-vis Pipelines
EPRI ePipe
EPRI WO8065-12
W2AGZ Technologies
...and...consider “recycling” CO2 emissions into alcohols!
Almost all NG used for electricity generation is “combusted” at a “local” delivery point using modern, efficient, combined cycle gas turbine (CCGT) technology.
Why not “combust” that gas portion so-used at the “well-head” instead and deliver the “electrons” over a low-loss HTSC dc cable? As well as
reducing volume of NG transported by pipeline.

## Slide 14: Power Delivery cost comparison between Gas/HVDC/LVDC-HTSC Technology Options
US cents/kWh
EPRI ePipe
EPRI WO8065-12
W2AGZ Technologies
HTSC ($5/kA-m @ 65 K) beats HVDC and Gas!
WOW!
Nota Bene! (That’s Latin for Preavviso) This figure contains 1997 “English/US” units for distance and currency and needs to be updated... Sega!
Marginal Cost of Power Delivery

## Slide 15
100 GW; +/- 100 kV; 500 kA
Nb3Sn; 4 K
1000 km
Garwin-Matisoo (1967)
Superconducting Cable Anthology
Garwin-Matisoo
Garwin-Matisoo IEEE
W2AGZ Technologies
EPRI ePipe
EPRI WO8065-12
W2AGZ Technologies
EPRI ePipe (1997)
5 GW; +/- 50 kV; 50 kA
Bi-2223; 68 K
1610 km
Dia. ~ 70 cm

## Slide 16
HTSC dc Cable
EPRI 1020458
W2AGZ Technologies
Dia. ~ 70 cm
EPRI Superconducting dc Cable (2009)
10 GW; +/- 50 kV; 50 kA
YBCO; 68 K
Constructed in 1 km segments

## Slide 17
So: Is there enough room underground for both wires and pipes?
Maybe even for a Train?

## Slide 18: USA/Canada
A Canadian’s View of the World!
The United States is Down Here!
The Mackenzie Valley Pipeline
1220 km
18 GW-thermal
2000 - ?

## Slide 19
“The Really Big Picture”
Electricity Conversion Assumptions
Wellhead Power Capacity | 18 GW (HHV)
Fraction Making Electricity | 33%
Thermal Power Consumed | 6 GW (HHV)
Left to Transmit as LNG | 12 GW (HHV)
CCGT Efficiency | 60%
Electricity Output | 3.6 GW (+/- 18 kV, 100 kA)
Cryo-Delivery
Co-Transmission (2006)
W2AGZ Technologies

## Slide 20: Opportunities to Exploit the Keystone XL Pipeline ROW for the Dual Transport of Chemical and Electrical Energy
Smart Grid
Fraternal Twins
2013 P. M. Grant’s Editorial in Smart Grid News

## Slide 21: Europe
Design/Deploy a Methane/Electricity ePipe Infrastructure to Socio-economically and Enviro-responsibly service the Emerging Energy Needs of the European Union
“A Modest Proposal”

## Slide 22
Where are the Opportunities?
Current European Natural Gas Fields/Pipelines

## Slide 23
o Wroclaw
The Wola Obszańska (Lublin) gas field in Poland/Ukraine was discovered in 1989. It began production in 1992 and produces natural gas. The total proven reserves of the Wola Obszańska gas field are around 37 billion cubic feet (1×109m³). “Dual-Pipe” to Berlin?
Scenario I

## Slide 24
Scenario II
Krio Odolanow
A hundred kilometres to the north-east of Wroclaw lies KRIO Odolanów, a branch of the Polish Oil and Gas Company, which operates the only installation in Europe for helium recovery from natural gas. The technology utilized in KRIO Odolanów is based on cryogenic processes and its two main products are liquid helium and liquefied natural gas.
...along the way, there’s...
So, why not extend the “Dual-Pipe” to Brussels? It is the European Union...

## Slide 25
”Polish-Ukraine-Pipe-Dream” vs. North American MVP Numbers
(Natural Gas Delivery Statistics...Sources/Comparisons)*
Sources | Reserves 109 cuft | Reserves Twh | wrt US | wrt MVP
US Total | 28,600 | 3.86105 | - | -
MVP | 7060 | 9.34104 | 25% | -
Lublin** | 37 | 5.00102 | 0.13% | 0.52%
*US-DOE-EIA: http://www.eia.gov/analysis/studies/worldshalegas/ Table I (note only proven reserves data are used, not possible recoverable shale deposits).
**https://en.wikipedia.org/wiki/Wola_Obsza%C5%84ska_gas_field (if nearby Ukrainian are available provable reserves were to be included, perhaps 5 times this number could be realized).
  ***See EPRI Report WO8065-12, March, 1997 (pdf), EPRI Report 1020458 (pdf), for possible HTSC cable designs.
Lublin – Berlin Pipeline Corridor “electrons/CH4 Energy Delivery ePipe Split”
Total Delivered Power (GW) | CH4 Portion (GW) | “electrons” Portion (GW)*** | CCGT efficiency – 50% (GW) | Years Until Exhaustion**
2.5 | 1.0 | 1.0 | 0.5 | 22.3
Scan the QR Codes in Bibliography for the references below...and then let’s discuss!

## Slide 26: Path Forward in the European Union
Present and Encourage Consideration/Study of the R-O-W Dual Use Concept by the Following EU Institutions:
  European Institute of Innovation & Technology (EIT)
  European Research Council (ERC)
  European Executive Agency (REA)
  Institute for Advanced Sustainability Studies (IASS)
Engage/Inform the R&D and Planning Staffs of Major European Gas & Electric Utilities and Their Equipment Suppliers:
  Gazprom; RWE; EDF Group (UK & France); E.ON; PGE (Poland)
  Siemens; BASF; ABB; Nexans; Prysmian Group
  European Pipeline Group (Ductile Pipes, Valves & Fittings)

## Slide 27
Engage Major European Technical Universities, Institutes and Companies Focusing on HTSC Power Application Development:
  KIT; MPI-Stuttgart; Université Paris-Sud
  CERN; CNR-INFM
  Nexans; Columbus Superconductors
Initiate, Investigate and Undertake Novel Technologies Relevant to the R-O-W Dual Use Concept:
  “Real Time” Recovery of H2O, CO2 from the “Tailpipe Emissions” of Wellhead CCGT Generators for Recycling into Methanol/Ethanol.
  Conduct Demonstration Projects Exploring the Efficacy of Co-transportation of Chemical and Electrical Power via a L-H2 (or L-CH4) Cooled HTSC “SuperGrid.” (Such as the H2 + MgB2 Cable Experiment Reported in Talk
  1A-LS-05).
  Finally, in Anticipation of the Exhaustion in 3-4 Decades of Recoverable Natural Gas Resources Throughout Europe, Explore the Efficacy of Re-using the Now-installed R-O-W Dual Use Delivery Infrastructure by Installing on the Sites of the Depleted Wellheads...

## Slide 28
...the Exploitation of Multi-century Reserves of Recyclable, Reprocessable, Proliferation-safe Thorium-based Nuclear Fission Generation of Electricity Accompanied by Hydrogen Production...aka
“The Energy Amplifier!”
Grazie Mille!
Stanford (2011)
W2AGZ Technologies
Energy Amplifier

## Slide 29: Bibliography

## Slide 30
What’s Next For Superconductivity?
Physics World interviews Paul Grant
Paul M. Grant
W2AGZ Technologies
Author
YouTube
Smart Grid
Fraternal Twins
2013 P. M. Grant’s Editorial in Smart Grid News
Upbraiding the Utilities
2011 P. M. Grant’s Editorial in Cold Facts
Cold Facts
Poster PDF
Dual Use
EUCAS 2013 Poster 2P-LS2-10
2012 AER
DOE AER 2012
W2AGZ Technologies
EPRI ePipe
EPRI WO8065-12
W2AGZ Technologies
Pipe-to-Power
EPRI TR-104787
W2AGZ Technologies

## Slide 31
HTSC dc Cable
EPRI 1020458
W2AGZ Technologies
Garwin-Matisoo
Garwin-Matisoo IEEE
W2AGZ Technologies
HTSC Power Apps
Cryo-Delivery
Co-Transmission (2006)
W2AGZ Technologies
Shale Gas Reserves
EIA Shale Data (2013)
Lublin Gas Fields
Wola Wikipedia
Stanford (2011)
W2AGZ Technologies
Energy Amplifier
Wroclaw (2010)
W2AGZ Technologies