Dual use of future natural gas pipeline rights-of-way for the 
transport of electricity via HTSC cables.

Paul M. Grant

W2AGZ Technologies
San Jose, California USA 95120

It appears likely that “clean” fossil fuels, exemplified by natural gas, given their current global abundance and accessibility, will continue to be exploited for at least the next two decades.  We discuss a scenario whereby future natural gas/petroleum pipeline deployment provides an opportunity for creating a common right-of-way to transport both chemical and electrical energy, the latter via high capacity HTSC dc cables.  Given the emergence of highly-Carnot efficient combined-cycle-gas-turbine (CCGT) generation technology, a significant portion of the natural gas delivered, perhaps as much as 40% or more, will be combusted at the end point to produce electricity.  It would be useful to contemplate generating this electricity “in bulk” at the gas field “well head,” taking into account the savings wrought by transmitting a lower volume fraction of gas with reduced frictional and pumping losses, and also economies of scale by concentrating CO2 capture and reprocessing at a single site, rather than at a multitude of gas delivery points.

We examine two proposed North American projects as potential “ePipeline” candidates, 1) a 1220 km natural gas pipeline to run from gas fields located on the Mackenzie River delta on the Artic shore of the Northwest Territories southward to a distribution infrastructure located in central Alberta, with a delivery capacity of 18 GW-thermal, and 2) an increased capacity build-out of  the existing Keystone pipeline, dubbed “Keystone XL,” to convey processed tar sand petroleum from Hardisty, Alberta, Canada, 3500 km southward to Houston, Texas.  Although the pipeline itself is designed for oil transport, there are large untapped gas shale fields near Hardisty that could be exploited for local CCGT electricity generation subsequently co-transmitted within the Keystone XL right-of-way.  In each case we will configure and parameterize the engineering economics appropriate to co-locating a 3 GW HTSC dc cable.

Lastly, we will suggest several European scenarios analogous to these two North American possibilities and briefly touch on combining liquid natural gas (LNG) and HTSC cryogenics, and eventually replacing well-head gas generation on depletion of the methane reserves with environmentally respectful nuclear fission power to produce hydrogen and electricity for delivery over the now-existing ePipeline delivery infrastructure.

Keywords: abstract; template; English; Chinese (maximum 4 key words)

能源挑战与力学国际研讨会摘要模板

John Smith1*，張三2 ，李四3

1School of Engineering, University of Aberdeen, Aberdeen, UK
2Department of Mechanical Science and Engineering, University of Illinois at Urbana-Champaign, Urbana, USA
3中国 北京清华大学工程力学系

文件定义了摘要的各个组成部分，包括标题和全部作者，以及每个作者的所在单位。作者列表中标有*号的为报告作者。请不要改变文件书写风格，包括字体和文字大小；不要在文件中使用特殊字符，符号或方程。

摘要将以英中文双语出现在研讨会文集里。美式和英式英文，简体和繁體中文都被认可。作者可以用英文或英中文双语（首选）提交摘要；如果只收到英文版本，我们将提供论文摘要的中文翻译。在英文版本的摘要中，单词总数必须在250到350之间。

论文摘要的版权属于作者。北海能源培训有限公司有权将摘要发表在会议网页网上和出版在本次会议的摘要文集里。

关键词：摘要；模板；英文；中文（最多4个关键词）